## Information Sheet 1

SAFETY RULES FOR THE SHAPER

The shaper can be one of the most dangerous machines in a wood working shop if safety rules are ignored.  The high-speed rotation of an exposed cutterhead should be enough to make every user practice the following rules.

- Follow General Shop Safety Rules

- Do not shape any stock that has metal or any foreign material on it.

- Do not shape any stock that is cracked, severely warped, or which contains knots.

- Lock out the power supply before you change the setup on the shaper or making adjustments.

- Be sure the fence is securely locked in place.  Make sure the cutter is clear of the fence. Double-check all attachments to make sure they are secure. Rotate the spindle by hand to make sure the cutter turns freely.

- Be sure cutter is securely locked on the spindle before starting machine, then test using the polycarbonate shield.

- Verify spindle rotation.  The spindle must turn in the correct direction relative to how the cutter is installed.

- Always feed the stock against the direction of the cutter rotation.  Feed with the grain of the stock whenever possible.

- Use a jig or holding fixture whenever possible.

- Do not attempt to make heavy cuts on the shaper.  Several light cuts may be necessary.

- Never have your hands closer than 4″ from the cutters. Use a push block or a jig for small or narrow pieces.

- Use feather boards or other hold-downs when shaping narrow pieces.  Better yet, rely on power feeders to secure and push stock through.  Not only is this safer, but you will get a better finish because it feeds at a constant rate.

- Install the cutter so that the bottom side of the stock—not the top—will be shaped when possible

- Use the smallest table insert possible as you want the smallest table opening at the cutterhead as possible.

- Position the infeed and outfeed fences so both will support the stock and be within 1/8” – ¼” of the cutting circle.

- Be sure the dust extraction is turned on and connected to the shaper

- Maintain a well-balanced stance and feed stock into the shaper at a steady rate.  Do not lean over the machine, and do not stop the feed or slow it down to the point where you overheat the cut.