Information Sheet 1

PORTABLE ROUTER SAFETY RULES

- Follow general machine safety rules.

- Unplug power cord when changing bits or adjusting the edge guide.

- Keep the power cord away from the bit.

- Always allow the motor to come to a complete stop before setting the router down.

- Do not attempt to take too heavy a cut.  Several light cuts may be necessary.

- Feed the router opposite the direction of cutter rotation.  Feed "with the grain" of the stock whenever possible.  If you must “climb-cut”, never remove more than ¼” of material at a time.

- Always check to see that the router is off before plugging in the power cord.

- Hold the router with both hands at all times if possible.

- Never turn the router on without a bit in the collet unless the collet and nut have been removed.

- When using router base templates, be sure the bit does not interfere with the template guide.

- Keep all ball-bearing pilots clean and lubricated.

- LET THE ROUTER COME UP TO FULL SPEED BEFORE THE BIT TOUCHES THE MATERIAL