Stationary Sander Teaching Notes (60”)

Aligned with checklist (10/19)

*Recommend students use checklist for notes during demo

Demonstration Videos: 	Spindle Sander (18:13)

Disk Sander (11:52)

Edge Sander (14:37)

Spindle Sander-inside curves, curves to straight-use fence

- Describe machine hazards & demonstrate lock-out/tag-out procedures

- On/off switch

- Oil level check vial

- Spindle selection and installation (demo both machines)

- Throat plate installation

- Explain how & when to change the abrasive

- Table adjustment (tilt)

- Demonstrate how to clean the machine & abrasives after use

Review

- Spindle/sanding sleeve mandrel (Changing Abrasives)

- Demo Using a fence

Additional Notes

- Do not interchange screw/taper inserts

- Use correct sized table insert for spindle

- Keep hands clear of spindle

- Do not force work and move material against spindle rotation

- Always keep a spindle in the machine to keep the dust out of the taper

- Review Exercise Criteria

Disk Sander-small parts and end grain

- Describe machine hazards & demonstrate lock-out/tag-out procedures

- On/off switch (discuss breaking issue)

- Table adjustments (Vertical, Horizontal, Tilt)

- Dry run of sanding

- Use of miter gauge

- Explain how to clean & change the abrasive

Additional Notes

- Use only the portion of the disk that travels down towards the table

- Do not hold work stationary against disk

- If disk is overheated it may gum up and burn work

- Clean disk

Edge Sander-longer straight parts, outside curves, face & edge-drawers

- Describe machine hazards & demonstrate lock-out/tag-out procedures

- On/off switch

- E-stop

- Oscillating switch

- Tracking knob (Remove abrasive, re-install & track)

- Miter gauge & adjustment of

- Sanding head height adjustment

- Extension table for large panels

- Demonstrate use of sander on a panel

- Demonstrate how to clean the belt & machine after use

Review

- Switch on/off & osculating, dust collection

- Drive & idler Rollers

- Platen

- Tracking

- Table tilt

- Belt tightening mechanism

Additional Notes

- Freehand – move work against the direction of travel - Light touch

- Keep work moving/oscillating

- Clean belt

- Sand against the grain(not with) if work is not cutting clean

- Edge sanding requires less pressure than face sanding

- Review Exercise criteria