Teaching Notes – Planer (60-70”)

(Items in Red align with Checklist)

Videos: Planer Demonstration – Part A (22:21)

Planer Demonstration – Part B (19:37)

- Purpose

- Obtain Parallel surfaces

- This machine will not remove warp – demo warped board

- Use in conjunction with the jointer

- Review with checklist

  - Describe machine hazards & demonstrate lock-out/tag-out procedures

    - Hearing & eye protection

    - LOTO – Lockout Oliver

    - Kickback

    - Pinch points

  - On/off switch

  - Identify the parts (Open up Oliver wide so students can see)

    - Infeed Roll (Corrugated vs. Rubber)

    - Chipbreaker

    - Cutter Head

    - Pressure Bar

    - Outfeed Roll

    - Discuss min part length = distance between infeed & outfeed rolls

  - Thickness adjustment

    - Discuss Backlash

    - Depth of cut gauge at DeWalt

  - Speed control

    - KMPI - Demo on two 18-24” pieces; compare under inspection light

    - Oliver

    - Format 4

    - DeWalt

  - Bed roller adjustment (Oliver only)

    - Help reduce friction

    - Adjustment of – too high = snipe, too low = difficulty feeding stock

  - What determines the minimum length of stock which can be fed?

  - Thickness scale calibration (check current reading).

  - What is the typical amount of material to be removed on a single pass?

  - Demonstration proper grain orientation using samples

  - Location of and proper use of a backer board

  - Dry run of planing (proper hand and standing position, proper depth setting relative to an actual sample)

    - Operations

      - Face Planing

        - Set Thickness; maximum stock removal

        - Stand to the side

        - Vary position for knife wear

        - Demo tapered board

      - Edge Planing

- Using jig for Oliver

- Run multiple pieces at once

      - Surfacing Thin Stock (3/8” or less)/Backer Board

    - Thickness measurements

      - Proper way to take a thickness measurement (snipe, taper)

      - Using Calipers; 1/16 is about equal to 0.063”

    - Other

  - Try to take equal amounts of wood off each face when planing

  - Use a depth of cut of 0.050” on the Felder for easy calculation

  - Limit depth of cut on DeWalt to 1/32”

  - Make sure dust collection is up to speed because the planer produces a large quantity of chips

□	Review Exercise Criteria

    - Parts of a planer