Teaching Notes - Band Saw (1:15”)

(1/19: Aligned with Checklist)

Videos: Band Saw Demonstration – Part A (17:47)

Band Saw Demonstration – Part B (12:41)

- S’s View PPT on their own. Parts:

- -Wheels & Wheel guards

- -Column

- -Table, table insert, miter groove

- -Table clamps, tilting feature

- - Blade guard & Adjustable Post with Locking Knob

- -Blade guides top & bottom, guide post

- -On/Off switch

- -Tensioning and tracking knobs

- -Fence

- -Throat depth

- –Motor

*stop at blade selection; watch Michael Fortune video on BB (4:00)

- Machine Demo (review with s’s using their checklists)

- Describe machine hazards & demonstrate lock-out/tag-out procedures

  - Safety; sawing force

  - Access Doors

  - Keep stock tight to the table

  - Never back out of a cut (short distance is OK, but watch the blade)

- Show the following controls:

  - On/Off switch

  - Blade guard Adjustment

  - Tension control

  - Tracking control

- What is the proper blade guide & thrust bearing adjustment?

  - Proper adjustment of the Blade Guard

    - Blade guard height – ¼” above stock.

    - Lower when done.

- Adjustment of the tilting table (if equipped)

- Dry run of cross-cutting with a miter gauge (proper hand position)

- Demo proper installation and use of a Pivot Block

- What is the proper cleanup after use? At the end of day?

- Other items:

- Wait till blade stops before removing small pieces from the throat plate

- Demo curved cutting

- Kerfing for tight radii

- Crosscutting with miter gauge

- V-block for ripping dowels

- Circle guide

- At Laguna, Wadkin:

- Show major controls for each machine (as above)

- Dry run of re-sawing  (proper hand position use of push stick) Resawing

- Use push stick when resawing

- Demo Resawing with a fence at Laguna, including adjusting for drift

- Show pivot block & flat fences for Resawing on Wadkin

- Blade – S’s review on their own

  - Watch video (6:46) on The Physics of Band Saw blades by Mathias Wandel (www.woodgears.ca) on BB or http://youtu.be/fK9m5PadmiI

  - Finish PPT on Blades

    - -Sizes

    - -Tooth Configuration-Skip vs. Hook

    - -Turning radii

- Review exercise criteria